6.5  Single Family Residential District (R-3)

a.   Purpose: The R-3 Single Family Residential District is

intended to provide a district which will allow residential

development in those areas where such development complies

with the Comprehensive Plan and policies.

b.   Permitted Uses: Within any R-3 District, no structure or land

shall be used except for one or more of the following uses:

1.   Single family detached dwellings.

2.   Public parks and playgrounds.

c.   Conditional Uses: Within any R-3 Single Family Use District,

no structure or land shall be used for the following uses

until a conditional use permit is approved.

1.   Any use as permitted and regulated in Section 6.4 c

(2-6) of this Ordinance.

2.   Two family dwellings, provided that public sanitary

sewer and water service is available and use therefore

and provided that the lot has a minimum width of 90 feet

and an area of 11,000 square feet.

d.   Permitted Accessory Uses: Within any "R-3" District, the

following uses shall be permitted accessory uses:

1.   Accessory uses as permitted and regulated in Section 6.3

(d) of this Ordinance.

e.   Lot Area, Height, Lot Widths and Yard Requirements:

1.   No structure shall exceed two (2) stories or twenty five

(25) feet whichever is least, in height except as

otherwise regulated by this Ordinance.

2.   A side yard abutting a public right-of-way (street)

shall not be less than fifteen (15) feet in width.  However, a fence is permitted in a side yard which abuts a public right-of-way if the fence is at least seven (7) feet from the public right-of-way, is no more than four (4) feet in height, and is constructed and maintained in a manner so that the fence can be seen through, with little or no loss of visibility (i.e., chain link).

The provisions of Section 4.7b and 4.7c, pertaining to the front yard, remain applicable.

3.   The following minimum requirements shall be observed

subject to additional requirements, exceptions and

modifications set forth in other sections of this

Ordinance.

Minimum Lot Area:                     8,250 square feet

Minimum Lot Width:                       65 feet

Front Yard Depth:                        53 feet from

center line of right-of-way

Side Yard Depth:                          4 feet

Rear Yard Depth:                         35 feet

Minimum Habitable Ground Floor Area     720 square feet